## Slide 1: UNIT IV
Framing, Flow Control, Error Detection & Correction, CSMA, CSMA/CD, HDLC and PPP

## Slide 2: Agenda
Framing, Flow Control Mechanisms
Stop Wait Protocol
Goback N ARQ, Selective Reject ARQ
CRC, Checksum
Types of Errors
Error Correction
CSMA, CSMA/CD
HDLC
PPP

## Slide 3: FRAMING
Data transmission in the physical layer means moving bits in the form of a signal from the source to the destination.
The physical layer provides bit synchronization to ensure that the sender and receiver use the same bit durations and timing
Framing in the data link layer separates a message from one source to a destination, or from other messages to other destinations, by adding a sender address and a destination address. Types of Framing
1. Fixed-Size Framing
2. Variable-Size Framing

## Slide 4: FRAMING
1. Fixed-Size Framing
In fixed-size framing, there is no need for defining the boundaries of the frames; the size itself can be used as a delimiter
Ex : ATM wide-area network
2. Variable-Size Framing
In variable-size framing, we need a way to define the end of the frame and the beginning of the next
Two approaches used to delimit the frame
i. a character-oriented approach
ii. a bit-oriented approach

## Slide 5: FRAMING
Character-Oriented Protocols
  The flag could be selected to be any character not used for text communication.
  In byte stuffing (or character stuffing), a special byte is added to the data section of the frame when there is a character with the same pattern as the flag.
  The data section is stuffed with an extra byte. This byte is usually called the escape character (ESC), which has a predefined bit pattern.
  Whenever the receiver encounters the ESC character, it removes it from the data section and treats the next character as data, not a delimiting flag.
  Byte stuffing and Unstuffing show in fig-1

## Slide 6: FRAMING(Fig-1)

## Slide 7: FRAMING
Bit-Oriented Protocols
  In a bit-oriented protocol, the data section of a frame is a sequence of bits to be interpreted by the upper layer as text, graphic, audio, video, and so on
  However, in addition to headers (and possible trailers), we still need a delimiter to separate one frame from the other.
  Most protocols use a special 8-bit pattern flag 01111110 as the delimiter to define the beginning and the end of the frame,
  A frame in a Bit oriented protocol shown in Fig below

## Slide 8: FRAMING

## Slide 9
Flow & Error Control

## Slide 10
Line Discipline: Determines which device can send and when it can send
Flow Control: Coordinates the amount of data that can be sent before receiving acknowledgement. Linked with error control
Error Control: Allows the receiver to inform the sender of any frames lost or damaged in transmission and coordinates retransmission of those frames by the sender
Data Link Control

## Slide 11: Line Discipline
In Line discipline whatever the system is, no device should be allowed to transmit until that device has evidence that the intended receiver is ready to receive the transmission
Line discipline can be done in two ways:
Enquiry/Acknowledgment (ENQ/ACK)
Poll/Select

## Slide 12
Second aspect of Data link control- Flow Control
Set of procedures that tells the sender as how much data it can transmit before waiting for an acknowledgment from the receiver.
Receiver got set of memory blocks called the BUFFER that store the incoming data before they are processed.
If buffer begins to fill up, receiver must be able to tell the sender to send fewer data frames or halt the transmission until the buffer is free to accept the data frame again.
Under this we got two techniques:
Stop- and Wait
Sliding Window
Flow Control

## Slide 13
In stop- and- wait flow control, the sender waits for an acknowledgment after every data frame it sends.
Only when acknowledgement has been received, the next data frame is sent.
The process of alternatively sending and waiting repeats until the sender transmits an end of transmission frame
Advantage: of stop and wait flow control is simplicity as each frame is checked and acknowledged before transmitting next frame
Disadvantage: It is very slow as each frame must travel all the way to the receiver and acknowledgement must travel all the way back before the next frame can be sent.
If distance between the devices are too long, time spent waiting for ACKs between each frame can add to the transmission time.
Stop and Wait

## Slide 15
In Sliding window, the sender can transmit several data frames before needing an acknowledgment
Frames can be sent one after another i.e. link can carry several frames at once and its capacity can be used efficiently
The receiver acknowledges only some of the frames using a simple ACK to confirm the receipt of multiple data frames
Sliding window is like an imaginary boxes at both the sender and receiver side
These windows can hold the data frames and provides the upper limit on the number of data frames that can be transmitted before receiving an acknowledgement.
Sliding Window

## Slide 16
Frames may be transmitted to the receiver as long as window is not full.
The frames are numbered 0 to n-1 . For example if n=8, frames are numbered 0,1,2,3,4,5,6,7,0,1,2,3,4,5,6,7,0,1………
The size of the window is n-1. Window always cover n-1 data frames and not n data frames.
When the receiver sends an ACK it can include the number of next frame it is expected to receive. For example when the sender sees an ACK with number 5, it means all frames upto 4 ( 0 to 4) has been received.

## Slide 17: Sender Window
At the beginning of transmission sender’s window contains n-1 data frames.
As frames are sent out, left boundary of window moves inward shrinking the size of the window
Given a window size w, if three frames have been transmitted since last ACK, number of frames left in window is w-3
For example say we have a window of size 7. ( 0 to 6)
Say Frames 0 through 3 have been sent and no ACK have been received, sender’s window contains only 4,5 & 6.
Once ACK is received with number 4, then four frames have been received ( 0 through 3) and sender’s window expands to include next four frames in buffer to contain totally 6 frames as 4,5,6,7,0,1,2.
If say received ACK is numbered 2, the sender’s window would have been expanded only by two frames to contain totally 6 as 2,3,4,5,6,7,0 only.

## Slide 18: Sender & Receiver Window

## Slide 19: Receiver Window
At receiver we got not n-1 data frames but n-1 spaces for frames
As new frames come in the size of the receiver window shrinks
Receiver window does not represent number of frames received but number of frames that may still be received before an ACK can be sent.
If a receiver got a window size of w, if three frames are received without being acknowledged , number of spaces in window is w-3.
As soon as ACK is received , the window expands to include more spaces for number of frames equal to number of frames acknowledged
Let us take the receiving window of size 7 i.e 0 through 6
With the arrival of data frame 0, receiving window shrinks moving from 0 to 1 and receiver window has now shrunk to six frames before sending an ACK
Once say frames 0 through 3 are received without sending an ACK, receiving window now shrinks to 3 frame spaces.

## Slide 20: Sliding Window

## Slide 21
Error correction in data link layer is implemented simply: anytime an error is detected in an exchange, a negative acknowledgement (NAK) is received and specified frames are transmitted- ARQ
Frame is so damaged because of noise and receiver cannot recognize the frame, ARQ allows us to say that the frame has been lost.
Other function of ARQ is retransmission of last frames including lost acknowledgement
Stop and wait is implemented as Stop and Wait ARQ
Sliding window is implemented as sliding window ARQ which comes under two variants: Go-back-n and Selective Reject
Automatic Repeat Request (ARQ)

## Slide 23
It is an extension of Stop-and –wait flow control to include retransmission of data in case of lost or damaged frames. For retransmission to work, four features are added:
Sending device keeps track of last frames transmitted until it receives an acknowledgment for that frame. Keeping a copy allows the sender to retransmit lost or damaged frames until they are received correctly
For identification purposes both data and ACK frames are numbered alternatively 0 and 1.
If an error is discovered in a data frame, indicating that it has been corrupted in a transit, a NAK frame is returned. When an NAK frame is returned, it resends the frame transmitted after the last acknowledgement irrespective of the number
Sending device is equipped with a timer. If an expected acknowledgment is not received within a allotted time period, sender assumes that last data was lost in transit and send it again
Stop and Wait ARQ

## Slide 24: Damaged Frames
when a frame is discovered by the receiver to be an error, it returns an NAK frame and sender retransmits the last frame again.
Let us take for example a sender transmits data frame and one of it is found to be an error.
Sender transmits data frame 0 and receives an acknowledgment ACK1 indicating it is expecting data 1
Now sends data 1 and receives acknowledgment ACK0
Sender now transmits next frame data 0 . Receiver discovers an error in it and returns an NAK
Sender retransmits data 0 again and receives ACK1.

## Slide 25
Damaged Frames

## Slide 26: ARQ- Lost Frames
Sender is equipped with a timer that starts every time the data frame is transmitted
If the frame never makes it to the receiver , the receiver can neither acknowledge it positively or negatively
Sending devices waits for an ACK or NAK until the timer goes off at which point it tries again
Now it retransmits the data frame and starts the timer once again and wait for an acknowledgement

## Slide 28: ARQ- Lost Acknowledgement
Here data frame has made it to the receiver has been found as either acceptable or not acceptable
But the ACK or NAK frame returned by receiver has been found to be lost in transit
Now the sending device waits until the timer goes off, then retransmits the data frame again.
Receiver here checks the number of new data frame.
If lost frame was a NAK, the receiver accepts the new copy and returns an ACK for it
If lost frame was an ACK, the receiver recognizes the new copy as a duplicate, acknowledges its receipt, discards the frame and waits for next frame.

## Slide 29: ARQ Lost Acknowledgement

## Slide 31
In Go-back-n ARQ, if a frame is lost or damaged all frames sent since last frame acknowledged are retransmitted
Similarly if an acknowledgment is lost, sliding window waits for the acknowledgement for some specified time. If acknowledgement does not arrive within the time, the data is retransmitted again
Go Back N ARQ

## Slide 32: Go-back-n: Damaged Frame

## Slide 33
We can see that six frames Frame 0,1,2,3,4,5 are being transmitted before an error is discovered in frame 3.
An ACK3 has been returned by receiver showing that frames 0,1,2 have been received undamaged. The ACK3 has been sent before data 3 has arrived
Data 3 is found to be damaged and so NAK3 has been sent immediately and frames 4 and 5 are discarded
Sending device now retransmits all frames 3,4,5 sent since last acknowledgement and process continues
Receiver discards frames 4 and 5 till it receive data 3 undamaged.

## Slide 34: Go-back-n: Lost Data Frame

## Slide 35
In this send five data frames 0 through 4 are transferred.
Two data frames data 0 and data 1 arrive intact but data 2 is lost
Next frame expected at the receiver is data 3.
Receiver is now expecting data 2 and so considers data3 to be an error and sends an NAK 2 indicating that 0 and 1 have been accepted but 2 is lost.
Data 4 is transmitted before receiving NAK2 which is out of sequence and is therefore discarded.
Once NAK2 is received, sender now retransmits 2,3,4.

## Slide 36: Go-back-n: Lost Acknowledgement

## Slide 37
In here the sender have transmitted first three frames 0 through 2.
An acknowledgment ACK3 is now being sent to the sender saying three data frames have been received.
The sender now waits a predetermined amount of time for an acknowledgment of three frames sent.
Once ACK3 is not received within this time, all data frames are retransmitted again.

## Slide 38
In selective reject ARQ, only specific damaged or lost frame is retransmitted
If a frame is corrupted in transit, NAK is returned and frame is resent out of sequence
Receiving device must be able to sort the frames it has and insert the transmitted frames into proper place in sequence
Selective Reject ARQ

## Slide 40
The sender transmits 6 data frames 0 through 5
Once data frames 0 and 1 arrives it is not acknowledged.
Once data 2 is found be damaged, NAK2 is sent which acknowledges that previously unacknowledged data frames that have arrived intact and current data frame is found to be damaged
NAK2 here tells that data 0 and 1 have been accepted and only data 2 has to be resent being damaged unlike go-back-n
Frames received after the damaged frames cannot be acknowledged until the damaged frames have been retransmitted
Receiver accepts data 3,4 5 while waiting for a new copy of data 2.
Once data 2 arrives undamaged, ACK5 can be sent acknowledging new data 2 and original data frames 3,4 and 5.
Logic is needed by the receiver to sort out of sequence transmission and keep track of frames are still missing and which have not yet been acknowledged

## Slide 41
Though retransmitting a specific damaged frame seem to be more efficient than resending all frames
Because of Complexity of storing and sorting required by the receiver and extra logic needed by sender to select specific frames for retransmission, Selective reject ARQ is expensive and not often used
Selective reject ARQ gives better performance but in practice it is usually discarded in favour of go-back-n for simplicity of implementation
Go Back N Vs Selective Reject ARQ

## Slide 42
Error Detection & Correction

## Slide 43
When an electromagnetic signal flows from one point to another it is subject to interference from heat, magnetism and other forms of electricity
This interference can change the shape of signal
When these signals is carrying binary data, such changes can alter meaning of data resulting in error.
Error when we say can be classified into two types- Single bit and Burst
Single bit error: Error where only one bit of given data unit such as byte, character or packet is changed from 0 to 1.
Burst Error : Error where two or more bits in a given data unit have changed from 1 to 0 or 0 to 1.
Error Detection & Correction

## Slide 44
Single Bit Error

## Slide 45
Burst Error

## Slide 46
Once a data is transmitted from sender to receiver, we need to check whether data received is error free or not.
For that we got some Error detection methods that is been used.
Some of them are :
Cyclic Redundancy Check (CRC)
Checksum
Error Detection Techniques

## Slide 47
Most basic method of error detection is to send every data unit twice
Receiving device would compare both versions of data unit
Any discrepancy would indicate an error and an appropriate correction mechanism could be set in place
This mechanism would be completely accurate but it would be slow.
This would double the transmission time and time it takes to compare bit by bit also must be added.
An improvement of this method is to include EXTRA INFORMATION FOR PURPOSE OF COMPARISON.
This technique is called Redundancy as extra bits are redundant to the information and discarded as soon as the accuracy of information is determined
Redundancy

## Slide 49
Four types of redundancy checks are used
in data communications

## Slide 50
Vertical Redundancy Check - VRC

## Slide 51: Performance
It can detect single bit error
It can detect burst errors only if the total number of errors is odd.

## Slide 52
Longitudinal Redundancy Check - LRC

## Slide 53
Performance
LCR increases the likelihood of detecting burst errors.
If two bits in one data units are damaged and two bits in exactly the same positions in another data unit are also damaged, the LRC checker will not detect an error.

## Slide 54
VRC and LRC

## Slide 55
The most powerful redundancy checking technique is CRC
This method uses binary division unlike LRC and VRC which uses binary addition.
In CRC instead of adding bits together to achieve a desired parity, Sequence of redundant bits called CRC or CRC remainder is appended to the end of data unit so the resultant data unit becomes exactly divisible by second predetermined number which is the divisor.
At receiver, incoming data unit is divided by the same divisor
If there is no remainder, data unit is assumed to be intact and accepted.
If there is a remainder it means data is been damaged in transit and must be rejected.
Cyclic Redundancy Check (CRC)

## Slide 56
CRC

## Slide 57: CRC Algorithm
First a string of 0’s appended to data unit. The number n is less than the number of bits in the divisor which is n+1
Secondly new elongated data is divided by the divisor using a process of modulo 2 binary division
Remainder resulting from division is CRC
CRC of n bits derived which is the remainder is appended to the data unit by replacing the appended 0’s
This data unit arrives at the receiver followed by CRC
Now the receiver divides the data unit by the same divisor to find the remainder
If remainder is 0 it means data is error free and is accepted
If remainder is non zero, data got error and is rejected.

## Slide 58: CRC Generator
CRC generator i.e. divisor is often represented as a string of 1s and 0s but as algebraic polynomial
Polynomial is represented as x7+ x6+ x4 +x3 +x +1
Relationship of polynomial to corresponding binary representation is 11011011
Standard CRC polynomials are CRC-12, CRC-16, CRC-ITU-T and CRC-32

## Slide 61
Polynomial

## Slide 62
Polynomial and Divisor

## Slide 63: CRC Example
Example: Suppose sender want to transmit the information string: 1111101. The receiver and sender decide to use the (arbitrary) polynomial pattern, 1101 which is the divisor

## Slide 64: CRC
Remainder is 0111 through modulo 2 division which is added to the data unit by replacing the appended 0’s to get 1111101000+ 0111= 1111101111
Receiver divides the appended data unit by the divisor to see if remainder is zero. If zero it is error free

## Slide 67
Error detection used by higher layer protocols is Checksum
Checksum also is based on the concept of redundancy
Check sum Generator :
In sender, checksum generator subdivides the data unit into equal segments of n bits usually 16
These segments are added together using one’s complement arithmetic so that total is also n bits long
The total is then complemented and appended to the end of the original data unit as redundancy bits called checksum bits
Checksum

## Slide 68
Checksum

## Slide 69: At the sender
The unit is divided into k sections, each of n bits.
All sections are added together using one’s complement to get the sum.
The sum is complemented and becomes the checksum.
The checksum is sent with the data

## Slide 70
The unit is divided into k sections, each of n bits.
All sections are added together using one’s complement to get the sum.
The sum is complemented.
If the result is zero, the data are accepted: otherwise, they are rejected.
At the Receiver

## Slide 71: Performance
The checksum detects all errors involving an odd number of bits.
It detects most errors involving an even number of bits.
If one or more bits of a segment are damaged and the corresponding bit or bits of opposite value in a second segment are also damaged, the sums of those columns will not change and the receiver will not detect a problem.

## Slide 72
Data Unit and Checksum

## Slide 73
Mechanisms covered till now would detect errors but not correct them
One method is when an error is detected by the receiver, the receiver can have the sender retransmit the entire data unit
Another technique is to have error correcting codes by the receiver.
These Error correcting codes are efficient to correct single bit error only
Not efficient in correcting a burst errors.
Based on this we will now see one of the famous Error correcting code- Hamming Code
Error Correction

## Slide 74: Hamming Code
Basic Idea:
  Codeword: Digital representation of a data symbol in transmission (e.g. A -> 01000001, & -> 00100110, etc.)
  Valid vs. Invalid Codewords: Set of codewords of same size (number of bits) used to interpret all data symbols is called valid codewords, while the set of codewords which does not belong to this set is called invalid codewords
    Both valid and invalid codewords are known to both sender and receiver in transmission
    A bit error can transfer a valid codeword to an invalid codeword
  Codeword = Data bits + Redundancy/Check bits
    Redundant bits are added to check whether the data is correct or some errors have been taken place
  Distance between codewords: The distance between two codewords Ci and Cj, denoted as Dist (Ci , Cj), is the number of bit positions, the codewords differ
    E.g. distance between codewords: 01101 and 10100 is 3

## Slide 75: Hamming Code
Basic Idea (Contd.):
  We can check whether a codeword is valid or invalid
Error Detection:
  For a single bit error detection, the distance between any pair of valid codewords must be at least 2
  Suppose C1 and C2 are two valid codewords and the distance between C1 and C2 is 1: C1 = 101101 and C2 = 101100 (the last bit differs)
  Due to single bit error in C2 in the last bit position, C2 becomes C1, also a valid codeword
    Error detection fails
  If the distance is 2, a single bit error still make their difference at least 1
    Error detection successful
  For detecting k errors, the distance must be at least (k+1)

## Slide 76: Hamming Code
Error Correction:
  Received codeword with bit errors can only be corrected if we can determine the bit positions where the bit errors have been taken place
    After correction, the received codeword will be converted to one and only one valid codeword
  For single bit error correction, the distance must be at least 3
Sent:
Received:
100100
100111
100101
100101
=
C1
C2
000100
100111
000101
100101
≠
C1
C2
100101
010101
001101
000001
000111
000100
Invalid codewords
Valid codeword
000101
110101
101101
100001
100111
100100
Invalid codewords
Valid codewords
Distance = 2
Distance = 3

## Slide 77: Hamming Code
Illustration of k bit Error Correction:
  For k bit error correction, the distance must be at least (2k+1)
Common Part
K bit
C1
C2
K bit
Common Part
K bit
K bit
K bit changed
K bit changed
Unchanged Part
Distance = 2k
Common Part
K bit
C1
C2
K bit
Common Part
K bit
K bit
K bit changed
K bit changed
Unchanged Part
Distance = 2k+1
1 bit
1 bit

## Slide 78: Hamming Code
Encoding and decoding technique developed by R.W. Hamming [1950]
  Up to one bit error correction and two bit error detection can be done
    Minimum distance in hamming code is 3
Number of redundancy bits (r) can be determined for a given data block size of ‘m’ bits by using the following formula:
For example, if m = 7, minimum of ‘r’ would be 4 as it satisfies the above equation: 24>= 7+4+1
Hence, the size of the codeword will be 7+4=11
To generate a hamming code, following steps are executed:

## Slide 79: Hamming Code
Step 1: Calculate the value of ‘r’ using the above formula
Step 2: All the redundancy bit positions are in the power of 2 (20=1, 21=2, 22=4, 23=8, .......) as shown below (where d is the data bit):
f8
f4
f2
f1
Step 3: Each data bit is included in a unique set of redundancy, as determined its bit position in binary form
a) Redundancy bit 1 covers all the bit positions whose binary representation includes a 1 in the least significant position (1 = 0 + 1, 3 = 0 + 1 + 2, 5 = 0 + 1 + 4, 7 = 0 + 1 + 2 +4, 9 = 0 + 1 + 8, 11 = 0 + 1 + 2 + 8, etc).

## Slide 80: Hamming Code
Step 3 (Contd.): b) Similarly redundancy bit 2 covers all the bit positions whose binary representation includes a 1 in the second position from the least significant bit (2, 3, 6, 7, 10, 11, etc)
c) Similarly, 4 covers 4–7, 12–15, 20–23, etc, 8 covers 8–15, 24–31, 40–47, and so on
To mark the dependent bit positions of the redundancy bits, we can prepare a table as follows:
Positions | f1 | f2 | f4 | f8 | ............
1 | × |  |  |  | 
2 |  | × |  |  | 
3 | × | × |  |  | 
4 |  |  | × |  | 
5 | × |  | × |  | 
6 |  | × | × |  | 
7 | × | × | × |  | 
8 |  |  |  | × | 
9 | × |  |  | × | 
10 |  | × |  | × | 
11 | × | × |  | × | 
.... |  |  |  |  | 

## Slide 81: Hamming Code
Step 4: Now we perform even parity check for each column of the above table. Set a parity bit to 1 to ‘f1’ if the total number of ones in the corresponding positions of its column is odd. Set a parity bit to 0 if the total number of ones in the positions it checks is even. Then, we repeat this process for ‘f2’, ‘f4’, ‘f8’ and so on.

## Slide 82
Example: Suppose we have to transmit a data block 7 bits: 1001101. We need to generate a hamming code of this data block.
Step 1: We need to determine minimum value of ‘r’ first, where 2r >= 7+r+1. We find r = 4.
Step 2: The codeword will be looked like as follows:
Step 3 & 4: Determination of redundancy bits:
f1 depends upon the bits in the positions of 3, 5, 7, 9, 11. Number of ones is 3, which is odd. To make it even, the redundancy bit f1 will be 1
f2 depends upon the bits in the positions of 3, 6, 7, 10 and 11. Number of ones is 4, which is even. So, the redundancy bit f2 will be 0
Following the similar procedure, the value of f4 and f8 will be 0 and 1 respectively
Hence the final codeword will be as follows:
11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
1 | 0 | 0 | f8 | 1 | 1 | 0 | f4 | 1 | f2 | f1
11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 1
Hamming Code

## Slide 83: Hamming Code
f1
f2
f4
f8
Illustration:

## Slide 84: Hamming Code
Error Detection and Correction:
Suppose in the above example the 5th bit is changed from 0 to 1 during data transmission, then it gives new parity values for the codeword:
Bit Positions | Number of 1s | New Parity values
f1,3,5,7,9,11 | 5 (odd) | 1
f2,3,6,7,10,11 | 4 (even) | 0
f4,5,6,7 | 3 (odd) | 1
f8,9,10,11 | 2 (even) | 0
11 | 10 | 9 | f8 | 7 | 6 | 5 | f4 | 3 | f2 | f1
1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 1
11 | 10 | 9 | f8 | 7 | 6 | 5 | f4 | 3 | f2 | f1
1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1
Sent bits
Received bits
The bits give the binary number as 0101 whose decimal representation is 5. Thus, the bit 5 contains an error. To correct the error the 5th bit is changed from 1 to 0.

## Slide 85: Hamming Code
Exercise 1: An error correcting code has the following code words: 00000000, 00001111, 01010101, 10101010, 11110000. What is the maximum number of bit errors that can be corrected?
Answer: Minimum hamming distance between any pair of codewords, d = 4 (check every pair). If maximum bit that can be corrected = k, then
d = 2k + 1,
4 = 2k + 1
K = 3/2 = 1.5, So maximum bit error that ca be corrected will be 1.

## Slide 86: Hamming Code
Exercise 2: Assume that a 12-bit Hamming codeword consisting of 8-bit data and 4-bit check bits is d8 d7 d6 d5 c8 d4 d3 d2 c4 d1 c2 c1, where the data bits and the check bits are given in the following tables:
Determine x and y.
Answer: Codeword is:
b1 ⊕ b3 ⊕ b5 ⊕ b7 ⊕ b9 ⊕ b11 = 0  c1 ⊕ d1 ⊕ d2 ⊕ d4 ⊕ d5 ⊕ d7 = 0  0 ⊕ 1 ⊕ 0 ⊕ 0 ⊕ x ⊕ 1 = 0  x = 0
b2 ⊕ b3 ⊕ b6 ⊕ b7 ⊕ b10 ⊕ b11 = 0  c2 ⊕ d1 ⊕ d3 ⊕ d4 ⊕ d6 ⊕ d7 = 0  1 ⊕ 1 ⊕ 1 ⊕ 0 ⊕ 0 ⊕ 1 = 0 (No x or y)
b4 ⊕ b5 ⊕ b6 ⊕ b7 ⊕ b12 = 0  c4 ⊕ d2 ⊕ d3 ⊕ d4 ⊕ d8 = 0  0 ⊕ 0 ⊕ 1 ⊕ 0 ⊕ 1 = 0 (No x or y)
b8 ⊕ b9 ⊕ b10 ⊕ b11 ⊕ b12 = 0  c8 ⊕ d5 ⊕ d6 ⊕ d7 ⊕ d8 = 0  y ⊕ x ⊕ 0 ⊕ 1 ⊕ 1 = 0  y =0
Data Bits |  |  |  |  |  |  | 
d8 | d7 | d6 | d5 | d4 | d3 | d2 | d1
1 | 1 | 0 | x | 0 | 1 | 0 | 1
Check bits |  |  | 
c8 | c4 | c2 | c1
y | 0 | 1 | 0
b12 | b11 | b10 | b9 | b8 | b7 | b6 | b5 | b4 | b3 | b2 | b1
d8 | d7 | d6 | d5 | c8 | d4 | d3 | d2 | c4 | d1 | c2 | c1

## Slide 87: Forward Error Correction (FEC)
Forward error correction (FEC) is an error correction technique to detect and correct a limited number of errors in transmitted data without the need for retransmission.
The sender sends a redundant error-correcting code along with the data frame.
The receiver performs necessary checks based upon the additional redundant bits.
If it finds that the data is free from errors, it executes error-correcting code that generates the actual frame.
It then removes the redundant bits before passing the message to the upper layers

## Slide 88: Advantages and Disadvantages
Because FEC does not require handshaking between the source and the destination, it can be used for broadcasting of data to many destinations simultaneously from a single source.
Another advantage is that FEC saves bandwidth required for retransmission. So, it is used in real time systems.
Its main limitation is that if there are too many errors, the frames need to be retransmitted.

## Slide 89: Types of FEC
Block codes
A block code encoder divides the information sequence "u" into message blocks of "k" information bits (symbols) and converts each message "u" into an n-bit code (symbols). The coding rate is defined as "R = k/n". The redundant bits (symbols), n-k, give the code the ability to deal with channel noise.
The minimum distance, dmin, between two closest codewords, which specifies the minimum amount of data changes required to turn one valid codeword into another, is an essential parameter of a block code. This parameter determines a code's ability to detect and rectify errors.
Usually, an FEC code can detect and correct up to
(dmin-1)/2 mistakes per codeword.

## Slide 90: Types of FEC
Convolutional codes
A convolutional code encoder accepts k-bit blocks of the information sequence "u" and generates an encoded sequence "v" of n-symbol blocks. However, each encoded block is dependent on "m" prior message blocks and the matching k-bit message block at the same time unit.
To provide reliable transmission across a noisy channel and redundant bits, n-k, further redundancy is added by raising the memory order "m" of the code.

## Slide 91
Medium Access control Methods –CSMA, CSMA/CA & /CD

## Slide 92: MULTIPLE ACCESS PROTOCOLS
When nodes or stations are connected and use a common link called a multipoint or broadcast link. We need a multiple-access protocol to coordinate access to the link.
The problem of controlling the access to the medium is similar to the rules of speaking in an assembly.
The procedures guarantee that the right to speak is upheld and ensure that
  Two people do not speak at the same time,
  Do not interrupt each other,
  Do not monopolize the discussion, and so on.

## Slide 93
Taxonomy of Multiple-Access Protocols

## Slide 94: Random Access Methods
In random access or contention methods, no station is superior to another station and none is assigned the control over another.
No station permits, or does not permit, another station to send.
At each instance, a station that has data to send uses a procedure defined by the protocol to make a decision on whether or not to send.
This procedure depends on the state of the medium whether it is idle or busy.

## Slide 95: Reason for Random Access or Contention
Two features give this methods its name
No scheduled time for a station to transmit and Transmission is random among the stations. So these methods are called random access.
No specific rules as which station should send next . Stations compete with one another to access the medium. So called Contention methods

## Slide 96: Procedure followed by Station for Random Access
Each station has the right to the medium without being controlled by another station
If more than one station tries to send, there is an access conflict- collision and frames will be either destroyed or modified
To avoid access conflict or to resolve it when it happens, each station follows a procedure which answers the following queries:
When can station access the medium
What can station do if medium is busy
How can the station determine the success or failure of the transmission
What can station do if there is an access conflict

## Slide 97
97
Random access methods we would be studying have evolved from a very interesting protocol known as ALOHA which uses a very simple procedure called Multiple Access (MA)
Method was later improved with the addition of procedure that forces the station to sense the medium before transmitting. This was called Carrier Sense Multiple Access
This later evolved into two parallel methods
Carrier Sense Multiple Access (CSMA)
Carrier Sense Multiple Access with Collision Detection and Avoidance (CSMA/CD) & (CSMA/CA)

## Slide 98: CSMA protocol
To minimize the chance of collisions and increase the performance, the CSMA (Carrier Sense Multiple Access) method was developed
CSMA requires that each station first listen to the medium before sending
CSMA can reduce the possibility of collision but cannot eliminate it.
Possibility of collisions still exists due to propagation delay
Two CSMA protocols developed were: Persistent and non-persistent

## Slide 99: Vulnerable time in CSMA
Vulnerable time in CSMA is the propagation time which is Tp i.e. time needed for a signal to propagated from one end to other.
When a station sends a frame and any other station sends a frame during this time, a collision will result.
But if the first bit of frame reaches the end of medium, every station will have heard the bit and will refrain from sending.
Figure in next slide shows the worst case where a frame sent by station A at time t1 reaches the rightmost station D at time t1+ Tp

## Slide 100: Vulnerable Time in CSMA

## Slide 101: Behavior of three persistence methods

## Slide 102: 1-Persistent CSMA protocol
When station finds the medium is idle, it sends its frame immediately with a probability of 1.
If the medium is busy it waits until it becomes idle and sends its frame with a probability of 1.
Method has highest chance of collisions because two or more stations may find the line idle and send their frames immediately.

## Slide 103: Non-persistent CSMA protocol
Station senses a channel
If channel is idle, station begins transmitting
If channel is busy, station does not continually wait for accessing the channel
Instead it waits a random period of time and then repeats algorithm again- Exponential Back off
This method reduces the collision as it is unlikely two or more stations will wait the same amount of time and retry to send simultaneously

## Slide 104: p-persistent CSMA protocol
This method is used if channel has time slots with slot duration equal to or greater than maximum propagation time
p-persistence approach combines the advantages of other two methods.
Reduces the chances of collision and improves efficiency
Here once the station finds the line is idle, it follows these steps:
i With probability p, station sends its frame
ii With probability q= 1-p, station waits for beginning of the next time slot and checks the line again
a. If line is idle, it goes to step i
b. If line is busy, it acts as collision has occurred and uses back off procedure.

## Slide 105: Flow Diagram of three persistence methods

## Slide 106: Carrier Sense Multiple Access with Collision Detection (CSMA/CD)
CSMA method does not specify the procedure following a collision
CSMA/CD augments the algorithm to handle collision
In this method, a station monitors the medium after it sends a frame to see if the transmission was successful
If successful, the station is finished
If not, frame is sent again.
We can better understand CSMA/CD with the diagram in next slide.

## Slide 107: Collision of first bit in CSMA/CD

## Slide 108
At time t1, Station A has executed the persistence procedure and starts sending the bits of its frame
At time t2 station C has not yet sensed the first bit sent by A .
Station C executes its persistence procedure and starts sending bits in frame which propagates to both left and right
Collision occurs after time t2.
Station C detects a collision at time t3
when it receives first bit of A’s frame.
Station C aborts its transmission
Station A detects collision at time t4 when it receives first bit of C’s frame; it also aborts its transmission immediately.
We see that A transmits for a duration of t4-t1; C transmits for duration of t3-t2.
At time t4 transmission of A’s frame though incomplete is aborted; time t3 transmission of C’s frame though incomplete is aborted

## Slide 109: Collision and abortion in CSMA/CD

## Slide 110: Minimum Frame size for CSMA/CD
For CSMA/CD we need restriction of the frame size
Before sending the last bit of frame, sending station must detect collision , if any must abort the transmission
Reason for this is a station once sent the entire frame does not monitor the line for collision detection
So, Frame Transmission time Tfr = 2 * Tp
If two stations involved in collision are maximum distance apart, signals from first takes time Tp to reach the second and effect of collision takes another time Tp to reach the first.
Requirement is first station should still be transmitting after 2 Tp

## Slide 111: Flow Diagram for CSMA/CD

## Slide 112
A network using CSMA/CD has a bandwidth of 10 Mbps. If the maximum propagation time (including the delays in the devices and ignoring the time needed to send a jamming signal, as we see later) is 25.6 μs, what is the minimum size of the frame?
Example
Solution
The frame transmission time is Tfr = 2 × Tp = 51.2 μs. This means, in the worst case, a station needs to transmit for a period of 51.2 μs to detect the collision. The minimum size of the frame is 10 Mbps × 51.2 μs = 512 bits or 64 bytes. This is actually the minimum size of the frame for Standard Ethernet.

## Slide 113: HDLC and PPP

## Slide 114: The Data Link Layer in the Internet
A home personal computer acting as an internet host.
Technology like Ethernet cannot provide “high-level” functionality like connection management and parameter negotiation

## Slide 115: Point to Point Data Link Control
One sender, one receiver, one link: easier than broadcast link:
    No Media Access Control
    No need for explicit MAC addressing
    E.g., dialup link, ISDN line
Popular point-to-point and high-level DLC protocols:
    PPP (point-to-point protocol)
    HDLC: High level data link control (Data link used to be considered “high layer” in protocol stack). HDLC is also used in multi-point links (one station many receivers)
These protocols can often be run over other data link technologies providing best of both worlds
  E.g., PPPoE, HDLC encapsulation by Ethernet

## Slide 116: PPP Design Requirements [RFC 1557]
Functionality : (similar to link layer services + extra management functions)
Packet framing - encapsulation of network-layer datagram in data link frame
  Multi-protocol - carry network layer data of any network layer protocol (not just IP) at same time ability to demultiplex upwards
Bit transparency - must carry any bit pattern in the data field (even if underlying channel can't)
Error detection - not correction

## Slide 117: PPP Design Requirements (cont.)
The extra stuff:
Connection liveness: detect, signal link failure to network layer
Network layer address negotiation: endpoint can learn/configure each other’s network address and other characteristics.
Authentication: who are you (or at least whose account do I bill for your dial-in time?)
  This information is used by traffic management software to control bandwidth to individual subscribers
Management features: loopback detection

## Slide 118: PPP non-requirements
No error correction/recovery
  (modems do one layer FEC, one layer packetization + retransmission “under the covers” anyway; other technologies are pretty reliable)
No flow control
Out of order delivery OK
Error recovery, flow control, data re-ordering
all relegated to higher layers!

## Slide 119: PPP Data Frame
Flag: delimiter (framing)
Address: ignored. (historical)
Control: ignored. (historical)
Protocol: upper layer protocol to which frame delivered (e.g., PPP-LCP, IP, IPCP, etc)

## Slide 120: PPP Data Frame
info: upper layer data being carried
check: cyclic redundancy check for error detection

## Slide 121: Byte Stuffing
flag byte
pattern
in data
to send
flag byte pattern plus
stuffed byte in transmitted data

## Slide 122: PPP Data Control Protocol
Before exchanging network-layer data, data link peers must
Configure PPP link (max. frame length, authentication)
Learn/configure network
layer information
  for IP: carry IP Control Protocol (IPCP) msgs (protocol field: 8021) to configure/learn IP address

## Slide 123: Where does PPP get used?
Dial-up – PPP over async serial, over modem
ADSL – PPP over Ethernet
Backbone – Packet over SONET (POS)
Why?
  Framing (dialup, POS)
  Efficiency (POS)
  Authentication, address negotiation (PPPoE)

## Slide 124: High-Level Data Link Control (HDLC)
HDLC was defined by ISO for use on both point-to-point and multipoint data links.
It supports full-duplex communication
Other similar protocols are
  Synchronous Data Link Control (SDLC) by IBM
  Advanced Data Communication Control Procedure (ADCCP) by ANSI
  Link Access Procedure, Balanced (LAP-B) by CCITT, as part of its X.25 packet-switched network standard

## Slide 125: HDLC Overview
Broadly HDLC features are as follows:
Reliable protocol
  selective repeat or go-back-N
Full-duplex communication
  receive and transmit at the same time
Bit-oriented protocol
  use bits to stuff flags occurring in data
Flow control
  adjust window size based on receiver capability
Uses physical layer clocking and synchronization to send and receive frames

## Slide 126: HDLC Overview
Defines three types of stations
  Primary
  Secondary
  Combined
Defines three types of data transfer mode
  Normal Response mode
  Asynchronous Response mode
  Asynchronous Balanced mode
Three types of frames
  Unnumbered
  information
  Supervisory

## Slide 127: HDLC
The three stations are :
  Primary station
    Has the responsibility of controlling the operation of data flow the link.
    Handles error recovery
    Frames issued by the primary station are called commands.
  Secondary station,
    Operates under the control of the primary station.
    Frames issued by a secondary station are called responses.
    The primary station maintains a separate logical link with each secondary station.
  Combined station,
    Acts as both as primary and secondary station.
    Does not rely on other for sending data

## Slide 128: HDLC
Primary
Secondary
Secondary
Commands
Responses
Combined
Combined
commands/Responses
Unbalanced Mode
Balanced mode

## Slide 129: HDLC
The three modes of data transfer operations are
  Normal Response Mode (NRM)
    Mainly used in terminal-mainframe networks. In this case,
    Secondaries (terminals) can only transmit when specifically instructed by the primary station in response to a polling
    Unbalanced configuration, good for multi-point links
  Asynchronous Response Mode (ARM)
    Same as NRM except that the secondaries can initiate transmissions without direct polling from the primary station
    Reduces overhead as no frames need to be sent to allow secondary nodes to transmit
    Transmission proceeds when channel is detected idle , used mostly in point-to-point-links
  Asynchronous Balanced Mode (ABM)
    Mainly used in point-to-point links, for communication between combined stations

## Slide 130: Non-operational Modes
Normal Disconnected Mode
Asynchronous Disconnected Mode
Both the above modes mean that the secondary node is logically disconnected from the primary node
Initialization Mode
  A node negotiates transmission parameters with the other node E.g., flow control information
  Parameters negotiated in this mode are used during any of the data transfer modes

## Slide 131: Data Link Control HDLC frame structure
(a) Frame
Format
(b) Control
field
format
Notes: 2

## Slide 132: Data Link Control HDLC frame structure
(c) Extended address field
(d) Extended control field
Notes: 2

## Slide 133: HDLC
Flag: 01111110- start and ending delimiter. Bits are stuffed for flags in data frames
FCS: 16-bit CRC using generating polynomial
  G(x) = x16 + x12 + x5 + 1
Address field:
  mainly used in multidrop link configuration, and not used in point-to-point
  In unbalanced configuration, every secondary is assigned a unique address. Contains address of secondary station in both command and response frames
  In balanced mode, command frame has destination address and response frame has sending node’s address
  Group addresses are also possible. E.g., One command sent to all the secondaries
In I-frames, N(s) is the sequence number of the frame being sent, and R(s) is the sequence number of the frame being expected.
The P/F bit, known as the poll/final bit, is used with different meaning in different contexts.
  It is used to indicate polling, to indicate the final I-frame, etc

## Slide 134: HDLC
There are three different classes of frames used in HDLC
  Unnumbered frames, used in link setup and disconnection, and hence do not contain ACK.
  Information frames, which carry actual information. Such frames can piggyback ACK in case of ABM
  Supervisory frames, which are used for error and flow control purposes and hence contain send and receive sequence numbers

## Slide 135: HDLC
There are four different supervisory frames
  SS=00, Receiver Ready (RR), and N(R) ACKs all frames received up to and including the one with sequence number N(R) - 1
  SS=10, Receiver Not Ready (RNR), and N(R) has the same meaning as above
  SS=01, Reject; all frames with sequence number N(R) or higher are rejected, which in turns ACKs frames with sequence number N(R) -1 or lower.
  SS=11, Selective Reject; the receive rejects the frame with sequence number N(R)

## Slide 136: HDLC
The unnumbered frames can be grouped into the following categories:
  Mode-setting commands and responses
  Recovery commends and responses
  Miscellaneous commands and responses

## Slide 137: Review of Link Layer
Services
  Framing
  Error control
  Reliability
  Connection management
  Medium access control
  Switching
Protocols, Standards
  Ethernet
  Token Ring
  FDDI
  Wireless
  PPP
  HDLC